## Slide 1
LLM-as-Multi-Robot-BT-Planner
Capability-Aware Generation of Synchronized Behavior Trees for Heterogeneous Robot Teams

## Slide 2
1. INTRODUCTION
The Problem: Programming Heterogeneous Robot Teams
Multi-robot teams improve efficiency and robustness by splitting subtasks across robots with different physical capabilities, BUT they are hard to program.
To manage multi-robot teams, we need to know:
  what actions to execute,
  which robot executes each one (capability-aware assignment),
  when inter-robot handoffs occur, and
  how robots synchronize, so noone acts on a precondition another has not yet produced.
Behavior Trees (BTs) are modular, reactive, and interpretable, but hand-designing them for heterogeneous teams is error-prone, especially the synchronization.
Research question. Given only a natural-language instruction and the initial world state, can an LLM generate synchronized, executable Behavior Trees for a heterogeneous multi-robot team with no task-specific planning aid?
2

## Slide 3
2. RELATED WORK
Where This Work Sits
LLMs for robot task planning
SayCan, ProgPrompt, PaLM-E: high-level decomposition and code generation. They generate flat action sequence for one robot (a list of skills to run in order). But we produce not just what actions, but which robot does each (capability-aware assignment), how they wait on each other (synchronization), and a full Behavior Tree per robot rather than a linear list.
LLM-based BT generation
Papers such as LLM-as-BT-Planner. We build on its use of schema constraints and structured feedback but extend the setting from single-robot trees to capability-aware assignment and inter-robot synchronization.
Multi-robot BT planning
MRBTP: cross-tree expansion and intention sharing, using an LLM only as an optional subtree pre-planner. We share its problem setting but invert the roles, making the LLM the sole planner and treating the symbolic machinery purely as a verifier.
Our position. The LLM generates the synchronized multi-robot BTs directly from the instruction, symbolic machinery is used purely as a verifier and not as a planner.
3
Behavior Trees in robotics
We adopt the standard BT execution semantics and node types as our output representation.

## Slide 4
3. BACKGROUND & METHODOLOGY
Problem Formulation
Scenario: S = (I, G, O, L, R)
  initial and goal states - I, G (sets of ground facts); objects - O; locations - L; team - R = {r₁,…,rₙ}.
Capability: c = (name, params, pre(c), eff(c)), eff = (add, del)
  PDDL-style add/delete templates.
State transition (the only operation that mutates state):
  w′ = (w \ match(del(c), θ)) ∪ ground(add(c), θ) — deletes before adds.
Plan: P = (T, A, Y, B)
  task graph - T, assignment - A: T→R, synchronization set - Y, BT forest - B (one tree per robot).
A plan is valid when
(V1) every assigned action is in that robot's capability set.
(V2) every precondition is supported - true in Initial state, produced earlier by the same robot, or produced by another robot and guarded by a sync Condition.
(V3) each inter-robot dependency in Y has a real upstream producer and its Condition placed before the consumer.
(V4) T is acyclic and each BT conforms to the node schema.
(V5) simulated execution drives “I” to “G” without deadlock.
V1-V4 checked statically
V5 by simulation
4

## Slide 5
4. OUR METHOD
The LLM Is the Planner, Code Only Verifies
Single-shot inference: the LLM emits the whole plan as one JSON object - task_graph, assignments, synchronization, behavior_trees. No deterministic synthesis or repair.
Back-chaining method (in prompt): domain-independent - from each unmet goal pick an add-effect, recurse until every precondition bottoms out at “I”, robot-scoped predicates (e.g. holding(r,x)) only created by “r” itself.
Synchronization = blocking guard: a Condition before a cross-robot dependency returns RUNNING (the robot waits).
Three task-agnostic reliability levers: the back-chaining method, best-of-N sampling, and two-stage generation (action plan, then BT encoding).
Pure vs. assisted ablation: “pure” = prompt + state + schema only; “assisted” injects producer hints (upper-bound baseline).
Generate
(best-of-N)
Validate
(typed errors)
Simulate
(deadlock-sound)
LLM
Self-correct
structured feedback + previous plan
5

## Slide 6
5. EXPERIMENTS
Evaluation Protocol (in progress)
Setting: symbolic simulation, actions update world-state predicates by the transition rule. Stochastic LLM → multiple independent trials, report rates and means ± std.
Two heterogeneous three-robot scenarios:
  Gear Assembly — 13 capabilities, 4 goal predicates, 3 cross-robot synchronization points.
  Sensor Calibration Cell — 19 capabilities, 6 goal predicates, substantially more synchronization.
Metrics: validity rate, goal-success rate, synchronization-error rate, mean correction rounds, generation time.
Generated trees exported to BehaviorTree.CPP XML - to real executors.
Ablation conditions
Pure, single-shot (C = 0)
Pure, self-correction (C = 4)
Pure, best-of-N (N = 4)
Pure, two-stage (action plan → BT)
Pure, combined
6

## Slide 7
6. RESULTS
Expected Outcomes (hypotheses to test)
Single-shot pure generation exposes the dominant failures.
Self-correction and best-of-N recover a large fraction of those failures.
Two-stage generation further raises goal success on the synchronization-heavy scenario.
Combined – combination of three methods, producing best results.
Condition | Valid | Goal | Sync Err. | Rounds | Time
Single-shot | — | — | — | — | —
Self-correction | — | — | — | — | —
Best-of-N | — | — | — | — | —
Two-stage | — | — | — | — | —
Combined | — | — | — | — | —
7

## Slide 8
6. CONCLUSION
Conclusion & Next Steps
An LLM infers the entire plan (task graph, capability-aware assignment, synchronization, and one BT per robot) from a natural-language instruction.
Deterministic code only verifies: a task-agnostic validator (typed error taxonomy) and a tick simulator returning a structured feedback that drives LLM’s self-correction.
Three domain-independent levers - back-chaining method, best-of-N, two-stage generation.
Next steps
Run scenarios in simulator to form a method’s comparison table.
Check if BTs are proper for ROS/real-robot testing.
Add real-robot execution via the BehaviorTree.CPP / ROS seam.
8